15Cxxx

DPTI 2015/0000/01

(author initials)

REQUEST FOR TENDER

SUPPLY AND DELIVERY OF PAVEMENT MATERIALS FOR

RN xxxx Xxxxxx – Xxxxxx (MM xx – xx.x)

| CONTACT FOR FURTHER INFORMATION | Tender enquiries are to be directed to: Mr/Ms …………………. Telephone: (08) 8343 2…… Mobile: … … … E-mail: …………@sa.gov.au If the above person is unavailable, the enquiry may be directed to: Mr/Ms …………………. Telephone: (08) 8343 2…… Mobile: … … … E-mail: …………@sa.gov.au |
| --- | --- |
| MANDATORY BRIEFING: | xx May 2015 at ……a.m./p.m. at .......... ..................... (refer Conditions of Tendering Annexure C for details) |
| CALL DATE: | xx May 2015 |
| TENDERS CLOSE AT | 2.00 pm on Tuesday/Thursday xx Xxx 2015, electronically at the Government Tender Website at www.tenders.sa.gov.au |

REVISION STATUS

| DOC REVISION | DATE | AMENDED PARTS | AMENDED CLAUSES |
| --- | --- | --- | --- |

If these documents are amended during tender call, the amended parts will be identified on this page and amendments will be denoted as follows:

- any deleted wording will be marked with strikeout and highlighted in grey; and

- any new wording will be highlighted in grey.

For each subsequent amendment, the formatting denoting the previous amendment will be removed so that only changes relating to the latest amendment are denoted.

_____________

INVITATION

On behalf of the Minister for Transport and Energy / Commissioner of Highways / Rail Commissioner (“Principal”), the Department of Planning, Transport and Infrastructure (“DPTI”) invites companies prequalified with DPTI for Supply of Pavement Materials in category P1, P2, P3 P4 (Aggregates), P5 (Sand) P6 (Recycled) and P7 (Mobile Crushing) (“Tenderer”) to submit tenders for the work described in the attached Specification.

CONTENTS

Conditions of Tendering

Schedule of Contract Documents

Specification

Annexure to the DPTI General Conditions of Contract: Supply of Goods

Tender Form

Schedules

____________

CONDITIONS OF TENDERING

The DPTI Conditions of Tendering (Edition: January 2015) are available from the following website and apply to this Tender:

http://www.dpti.sa.gov.au/documents/contractsandtenders/specifications_-_conditions_of_tendering

Please note:

- Annexures to the Conditions of Tendering are included in this document and are to be read in conjunction with the Conditions of Tendering from the above website.

____________

CT ANNEXURE A

TENDER SUBMISSION

TENDERERS MUST SUBMIT THE FOLLOWING WITH THE TENDER:

Tender Form

Schedule Checklist

The following Schedules:

- Schedule of Rates.

- Certificate of Currency of Public and Product Liability Insurance.

- Confirmation of the ability to supply the material within the timeframe specified.

- Location of the Quarry.

- Employment Contribution Test – Metropolitan / Regional

NUMBER OF COPIES TO BE SUBMITTED:

The Tenderer shall wherever possible compile their submission into one .pdf document.

____________

CT ANNEXURE B

ASSESSMENT OF TENDERS

The tender assessment process will follow the general approach of “Comparative Price" Methodology, as described in the DPTI Tender Evaluation Guidelines, available from:

http://www.dpti.sa.gov.au/documents/contractsandtenders/guidelines_and_miscellaneous

Tenders will be evaluated in accordance with the following criteria:

- Ability to supply the material within the time specified.

- Location of the quarry.

- Suitability of material tendered.

- Price.

The above is only a summary of the evaluation process and other factors may be taken into account in the selection of the successful Tenderer.

____________

CT ANNEXURE C

SUPPLEMENTARY INFORMATION FOR TENDERERS

1.	BRIEFING

A pre-tender meeting is scheduled for 1 October 2009 at 9.30a.m at Hutchens Road, Woodside (adjacent to the soccer pitch) to discuss potential hazards in relation to off loading of the pavement materials for this contract.

### 2.	AWARDING OF CONTRACTS

The Principal reserves the right to accept the whole or any part of the tender at the rate quoted and may award contracts to more than one Contractor.

____________

SCHEDULE OF CONTRACT DOCUMENTS

The Goods shall be supplied in accordance with the following documents, which comprise the Contract in accordance with the General Conditions of Contract:

- Formal Instrument of Agreement.

- Letter of Acceptance of Tender.

- Specification.

- General Conditions of Contract: Supply of Goods (Edition: March 2015) available from http://www.dpti.sa.gov.au/contractor_documents/dtei_general_conditions_of_contract

(Note: The Annexure to these General Conditions is included in this document and replaces the one listed at the above website)

- Tender Form.

- Schedules.

| 1 | Schedule Of Rates |
| --- | --- |
| 2 |  |
| 3 |  |
| 4 |  |

- Any correspondence referred to in the letter of acceptance of tender.

___________

SPECIFICATION

INTRODUCTION

The Specification for this Contract comprises of Part 1 and the following parts of the DPTI Master Specification for Transport Infrastructure (“DPTI Master Specification”).  Any Contract Specific Requirements for a DPTI Master Specification Part will be included in Part 1.

| Part No. | Title | Revision Status |
| --- | --- | --- |
| G20 | Quality System Requirements * | April 2013 |
| G30WHS MP | Work Health and Safety Management Plan * | December 2012 |
| R15 | Supply of Pavement Materials** | August 2014 |
| R15 | Attachment 1** | April 2014 |

* Available from http://www.dpti.sa.gov.au/contractor_documents/specifications_-_division_1

** Available from http://www.dpti.sa.gov.au/contractor_documents/specifications_-_division_2_roadworks

A reference to Superintendent in a DPTI Master Specification Part means a reference to the Principal’s Representative for this Specification.

_________

PART 1

GENERAL

CONTENTS

- Scope and Nature of Contract

- Supply, Delivery and Measurement

- Preparation of Stockpile

- Contract Specific Requirements for DPTI Master Specification Part

- Rise and Fall

- Payment

- SCOPE AND NATURE OF CONTRACT

This Contract is a Schedule of Rates Contract for the supply and delivery of pavement materials as detailed in Schedule 1 for RN xxxx xxxxxxxxxxxx (MM xx – xxx4), between the townships of xxxxxxxxx  and xxxxxxxxxxxx.

The Contractor will be advised of the quantity of material for each of these items prior to the commencement of the work.

The Principal reserves the right to award the Contract to more than one Contractor.  Where Contracts are awarded to more than one Contractor, the quantities of materials to be delivered shall be as stated in the letter of acceptance of tender.

- SUPPLY, DELIVERY AND MEASUREMENT

  - Materials Required

The designated quality requirements of each product shall meet the requirements of Part 215 "Supply of Pavement Materials".

Type A Fill material shall be classified in accordance with the following table:

| Classification | A |
| --- | --- |
| Material Source | Sand-clay Sand, Rubble, Quarry or Pit Overburden or By-product |
| Max. Particle Size (mm) | 75 |
| Grading (% passing) 75 37.5 0.075 | 100 80-100 0-25 |
| Max. Plasticity Index | 12 |
| Max. Linear Shrinkage | 6 |
| Max. Weighted Plasticity Index (1) | 1 000 |
| Mica, shale and similar laminated materials (3) | Not permitted |

Notes:

(1)	The Weighted Plasticity Index (WPI) is defined as the value of the plasticity index (PI) times the % passing the 425 micron sieve.  The Contractor shall provide the calulations for the WPI.

(2)	Mica, shale and similar laminated materials, adherent coatings or other foreign material shall not be present in form or sufficient quantity to produce adverse effect upon the usage and performance of the material.

The Contractor shall be able to supply a minimum of 1000 tonnes of material per day, if required.

Each Lot of material shall have an assigned maximum dry density as described in AS 1289.5.4 and DPTI test procedure MAT-TP-166 “Assignment of Maximum Dry Density and Optimum Moisture Content Values”.

The Principal’s Representative will give the Contractor a minimum of 3 working days notice for all orders to be delivered.

For the purpose of this Clause the Principal’s Representative will be the DPTI Work Supervisor.

  - Delivery

Alternative 1

The Contractor shall make arrangements with the Principal’s Representative prior to delivery and deposit the material within the Depot as designated by the Principal’s Representative.

The Contractor shall deliver only during normal DPTI working hours.

For the purpose of this Clause the Principal’s Representative will be the DPTI Work Supervisor.

Alternative 2

Deliveries shall not commence until the material conforms to the material specification, and the prepared lot has been inspected by the Principal’s Representative.

The Contractor shall deliver material to MMxx (Location of stockpile) / the worksite.

Deliveries shall commence from xxxxxx…….

The Contractor shall provide documented evidence that the quantities specified have been delivered.

Failure by the Contractor to deliver the material when ordered and at the rate stated shall constitute a non-conformance.  The Contractor shall advise the Principal’s Representative as soon as the non-conformance is detected and advice of the corrective action initiated.

  - Method of Measurement

Alternative 1

Measurement of material shall be by weighing at a licensed weighbridge.  Weigh notes shall be supplied to the Principal’s Representative.  (A licensed weighbridge is one that complies with all relevant Acts in the State of South Australia).

For the purpose of this Clause the Principal’s Representative will be the DPTI Work Supervisor.

Alternative 2

The Contractor shall have an automated weigh device for the measurement of each truck load of product delivered to stockpile.  The device shall generate a printed record of the quantity measured.

The Contractor shall arrange for calibration of the device prior to the commencement of deliveries.  The Contractor shall provide written evidence of the accuracy of the device to the Principal’s Representative prior to commencement of deliveries.  (Evidence acceptable to the Principal’s Representative includes a certificate from a Registered Repairer of Weighbridges, or a docket from a Registered Weighbridge for a truck load of product that verifies the accuracy of the device to within ( 1%.).

The Principal’s Representative may direct that the accuracy of the device be checked at any other time during the Contract by weighing a load of product.  The Contractor shall be entitled to reimbursement of any additional expense incurred if the reweighing is not more than 2% below the weight indicated by the device.

The Contractor shall provide documented evidence that the quantities specified for the Stockpile Site have been delivered.  Conversion factors to convert tonnes to cubic metres, if used, shall be supported with documented evidence of their derivation.

The Principal’s Representative will conduct audits on the volume of material delivered to the stockpile.  Payment will be made for the volume of material measured by the Principal’s Representative where this is less than the delivered quantity advised by the Contractor.  The Contractor may be in attendance during stockpile measurement.  Upon request, the Principal’s Representative will make available to the Contractor results of stockpile measurement audits for use in determining conversion factors.

Payment will be made for the delivered quantity in stockpile, but shall be limited to the lesser of 10% or 10 cubic metres above the quantity specified.

Separate payment will not be made for measurement.

Alternative 3

The Contractor shall have an automated weigh device for the measurement of each truck load of product delivered.  A record of the quantity measured shall be provided.

The Contractor shall arrange for calibration of the device prior to the commencement of deliveries.  The Contractor shall provide written evidence of the accuracy of the device to the Principal’s Representative prior to commencement of deliveries.  (Evidence acceptable to the Principal’s Representative includes a certificate from a Registered Repairer of Weighbridges, or a docket from a Registered Weighbridge for a truck load of product that verifies the accuracy of the device to within ( 1%.).

The Principal’s Representative may direct that the accuracy of the device be checked at any other time during the Contract.  The Contractor will be entitled to reimbursement of any additional expense incurred if the reweighing is not more than 2% below the weight indicated by the device.

- PREPARATION OF STOCKPILE SITE

The preparation of the area for the stockpile site at the point of delivery will be the responsibility of the Principal.

The Contractor shall protect the quality of product during all stages of processing occurring after sampling and testing.  The Contractor shall undertake methods of handling that prevent damage, deterioration or contamination of the product between the time of testing through to delivery.

The Contractor shall be responsible for the stockpiling of the delivered material to the following requirements:

(1)	The stockpiles are to be contained within the prepared stockpile area in a manner that allows access to at least 2 sides of each stockpile.

(2)	The stockpiles shall be constructed by adding material in layers if required, with each layer fully contained within the area occupied by the upper surface of the preceding layer such that a small berm approximately one metre in width is retained at each layer.

(3)	Levelling of each layer shall be the responsibility of the Contractor and shall be carried out in a manner to minimise segregation and material breakdown.

Additional payment will not be made for stockpiling and leveling of stockpile layers.

- CONTRACT SPECIFIC REQUIREMENTS FOR DPTI MASTER SPECIFICATION PART

G30WHS MP	WORK HEALTH AND SAFETY

Insert any known hazards here e.g.

The location of the works and the crossfall of the existing road may present a danger to the unloading of material using semi trailers.

At a number of the sites particularly on the Fleurieu Peninsula have reduced sight distance on the road approaches.  The Contractor shall provide appropriate traffic control signage at these and any other appropriate sites whilst deliveries are occurring.

- PAYMENT

  - General

Payment will be made in accordance with the Schedule of Rates.

  - Rise and Fall

  - Invoicing

The Contractor shall invoice the Principal by submitting the invoice to Shared Services via one of the following methods:

  - Post: PO Box 11027, Adelaide, 5001.

  - Email (PDF format):	APinvoices@sharedservices.sa.gov.au

The invoice shall clearly identify:

- The Principal supplied Purchase Order number as stated on the Letter of Acceptance of Tender.

- The Contract number “XXCxxx”.

- The words “Field Services”.

- The location and date/s of work

- Clear, itemised details of all work requiring payment

Invoices shall comply with the requirements of the Australian Taxation Office Guidelines available for downloading from:   www.ato.gov.au/businesses/content.asp?doc=/content/50913.htm

___________

GENERAL CONDITIONS OF CONTRACT

General Conditions of Contract: Goods (Edition: March 2015) applies to this Contract and is available from http://www.dpti.sa.gov.au/contractor_documents/dtei_general_conditions_of_contract

(Note: The Annexure to these General Conditions are included below and replaces the ones listed at the above website)

# ANNEXURE

______________

TENDER FORM

TO THE GENERAL MANAGER:

THE SUPPLY & DELIVERY OF PAVEMENT MATERIALS FOR

RN xxxx Xxxxxx – Xxxxxx (MM xx – xx.x)

I/We the undersigned, do hereby tender to perform the above mentioned services in accordance with the Tender Documents.

| Tendered Sum (exclusive of GST) | $ |
| --- | --- |
| GST amount | $ |
| Tendered Sum (inclusive of GST) | $ |

I/We acknowledge the receipt of amendments numbered:...........................................

(Tenderer to insert number of amendments received)

Tenderer's Name ..................................................................................................................................

(BLOCK LETTERS)

ACN ......................................................................... ABN .................................................................

Address ...........................................................................................................................................................

Telephone No. ................................................................................................................................................

Contact E-mail Address ……………………………………………………………………………………..

Signature of Tenderer ............................................................ Name .................................................................

Position in Company ...........................................................................................................................................

Signature of Witness ..................................................... Name of Witness ........................................................

Dated the .......................................................................... day of ................................................... 20 .............

FOR OFFICE USE ONLY

................Submission(s) opened on ............./............/2015 By: .................................................................... ........................................................... (Signature of Authorised Officer) (Printed Name of Authorised Officer) And: .................................................................... ........................................................... (Signature of Authorised Officer) (Printed Name of Authorised Officer)

TENDER FORM (CONTINUED)

DECLARATION IN RELATION TO UNLAWFUL COLLUSION

Re: DPTI XXCxxx

I, ………………………………………….…………….of …………………………………………………………….

[insert name and address of declarant]

do hereby declare as follows:

- I hold the position of ………………………………………………………………………..within

…………………….. ……….………………….. ………………………………………(Tenderer)
 and that I am authorised to provide this declaration on its behalf.

- I confirm that the tender submitted by the Tenderer is independent and that there has not been any unlawful collusion with any other tenderer or party in connection with this tender process. This clause does not apply to any formal joint venture contractual arrangement entered into between the Tenderer and any other person(s), the details of which have been provided to the Principal as part of the tender submitted by the Tenderer.

- I confirm that the total value of the goods and/or services to be provided by subcontractors, to the extent known at the time of making this declaration, is $...................

- Where subcontract work comprises more than 25% of the value of this tender, attached hereto is a complete list of all sub-contractors, the value, and the nature of the work to be provided under each sub-contract, to the extent known at the time of making this declaration.

- I understand that if any part of this declaration is found to be false the Principal reserves the right (regardless of any subsequent dealings) to:

- terminate negotiations with the Tenderer;

- terminate consideration of the Tenderer’s bid; and

- terminate any contract between the Tenderer and the Principal in relation to the Project without any obligation on the Principal to make any payment to the Tenderer.

……………………………………….				……../……../ 20 …

Signature								Date

Note: If the tender is submitted jointly with another party or parties, each party must sign this declaration.

##### SCHEDULE CHECKLIST FOR TENDER SUBMISSION

##### For each item please tick the box to indicate that the Schedule has been completed in accordance with Conditions of Tendering Annexure A and included with your tender submission.

| 1 | Schedule of Rates. | □ |
| --- | --- | --- |
| 2 | Certificate of Currency of Public and Product Liability Insurance. | □ |
| 3 | Confirmation of the ability to supply the material within the timeframe specified. | □ |
| 4 | Location of the Quarry. | □ |
| 5 | Employment Contribution Test - Metropolitan / Regional | □ |

SCHEDULE 1

SCHEDULE OF RATES

Amounts shall be exclusive of GST.

| Item | Description | Quantity and Unit of Measurement | Rate ($) | Amount ($) |
| --- | --- | --- | --- | --- |
| 1. | PM1/20 | 2100 (+/- 30%) tonne |  |  |
| 2. | PM2/20 | 1000 (+/- 30%) tonne |  |  |
| 3. | SPM20C2 | 1000 (+/- 30%) tonne |  |  |
| 4. | SPM20C4 | 1100 (+/- 30%) tonne |  |  |
| 3. | Sa- C | 50 (+/- 30%) tonne |  |  |
| 4. | Type A Fill | 500 (+20%/-100%) tonne |  |  |
| 5. | Additional Rate for Tandem deliveries | tonne |  |  |
| Total $ |  |

SCHEDULE 5

EMPLOYMENT CONTRIBUTION TEST

Download the Metropolitan / Regional South Australian Employment Contribution Test Template
available from: http://dpc.sa.gov.au/south-australian-industry-participation-policy.

This must be submitted as a separate .pdf file.

# Comments

Include Contract Manager and document author initials.

e.g JE / RE

Refer to template PR350-2 for the covering letter for this RfT

Include nearby towns so that Tenderer gets an appreciation where the job is.

A second contact person must always be included

Delete entire line if no briefing

Only include this reference to Annexure C if special requirements for the meeting; eg safety apparel

Delete if not applicable.

Specifier to check and amend as necessary.

Applicable for all procurements

>$22K and <$1M (Regional)

>$22K and <$4m (Metropolitan)

Specifier to select

This Annexure is not usually required.

Only include if there are special requirements eg multiple contracts to be awarded from a single tender call

Only include this clause if multiple contracts may be awarded

Not normally required for jobs under $550k & low risk.

Specifier to check and amend as necessary.

Specifier to complete

Specifier to review and update Revision Status of each Part as applicable..

This Part is required due to clause relating to compliance with Part 4 of the Road Traffic Act which is not detailed in Clause 27 of the GCC.

Any Contract Specific Requirements are to be inserted in this Part.

To be reviewed after compilation of this Part 1

Delete if not applicable

Insert only if applicable.

Use if more than one supplier possible

If Type A fill required

Specifier to address.

Specifier to select Alternative 1 or 2.

Specifier to address

Specifier to address

Specifier to select Alternative 1, 2 or 3.

Delete if not required.

Delete if not applicable

Delete if not applicable.

Note that OHS&W is spelt out in clause 30 of the GCC. Only place site specific hazards here if they exist.

Only to be used if GCC Goods clause 16 & 18 is insufficient or additional information is required to be added.

Only to be used if R&F is applicable, otherwise delete (refer GCC).

Insert DPTI Section name

Specifier to check and amend as necessary.

Copy and paste Annexure from GCoC Goods available at:

http://www.dpti.sa.gov.au/contractor_documents/dpti_general_conditions_of_contract

and complete details required in the Annexure

Copy title from Cover sheet and change font to TNR

Insert Contract Title

Include if Contract value exceeds $1,000,000 (GST inc)

Specifier to construct in accordance with Conditions of Tendering Annexure A.

Specifier to select

Only use classifications that are in accordance with Part R15

Don’t forget to add “W” in accordance with R15 if wet mixed material is required.

Specifier to select